## Slide 1: Project Title: Designing a Secure and Scalable AWS Cloud Infrastructure
Course: INFO2350 - Advanced Cloud
Group: Section 2 - Group 4
Team Members:
Maharshi Parekh (8992478)
Dhrumit Vekariya (8918788)
Cristian Osorio Vera (8903136)
Parth Trivedi (8827151)
Date: August 05, 2025

## Slide 2: Project Overview
Objective: Design and deploy a secure and scalable AWS infrastructure for a web application and backend database.
Key Requirements:
Custom VPC with public/private subnets
EC2 Web Server in public subnet
RDS Database in private subnet
Secure routing and access control
Automation using Terraform (IaC)

## Slide 3: Task 1 Architecture Diagram
VPC Name: MYPROJECT-IGW
CIDR Block: 172.31.0.0/16
Subnet Division:
Public Subnets (3) - 172.31.1.0/24, 3.0/24, 5.0/24
Private Subnets (3) - 172.31.2.0/24, 4.0/24, 6.0/24
Availability zones: us-east-1a, 1b, 1c
Purpose: Separate web and database layers, allow secure communication, and access the internet.
Link: https://app.eraser.io/workspace/BmGH6gxF2f8BMwqtfuqn?origin=share

## Slide 4: Key AWS Resources & Roles
Internet Gateway (IGW): Provides public access to web servers
NAT Gateway (NAT GW): Allows private resources to access internet (for updates)
Web EC2 instance:
Elastic IP
Apache server (httpd) installed
Outputs "Hello from WEBSERVER-MYPROJECT"
Database (EC2 or RDS):
Resides in private subnets
Accepts traffic from Web EC2 only through port 3306 or 5432
Security Groups:
Web SG: Open ports 80, 443, 22
DB SG: Allows access from web SG only

## Slide 5: Implementation of AWS Cloud Infrastructure
Objective: Deploy a secure, scalable AWS environment based on our architecture.
Key Components Configured:
Custom VPC with public and private subnets
EC2 Web Server in Public Subnet
RDS/DB Server in Private Subnet
Route tables and Security Groups
Tools Used: AWS Management Console(Learner Lab)

## Slide 6: VPC, Subnets, Routing & Web Server Deployment
VPC Name: MyProject-IGW
CIDR Block: 172.31.0.0/16
Components Configured:
6 Subnets (3 Public, 3 Private)
Internet Gateway attached
Public Route Table with explicit subnet associations
Purpose: To enable public web server access & private DB isolation

## Slide 7: Routing & Subnet Association
Route Table: MyProject-rtb-public
Public Subnets Associated:
Subnet-A, Subnet-B, Subnet-C
Subnet Example: PrivateSubnet-A
Public subnets routed via Internet Gateway
Private subnets kept internal (no IGW route)
Connectivity:

## Slide 8: EC2 Setup & Web Access Verification
EC2 launched in Public Subnet
Apache Installed: Verified via CLI
SSH Access: Achieved via PuTTY (Amazon Linux 2023)
Test Result : Browser displays hosted index.html (web app confirmed running)
Security Group: Allows HTTP/SSH from anywhere

## Slide 9: Task 3 AWS Infrastructure Automation Using Terraform
Content:​
Goal: Automate the creation of a basic two-tier AWS infrastructure using Terraform​
Environment: AWS Learner Lab(temporary credentials configured locally)​
Tool Used: Terraform v1.12.2 (CLI on Windows)

## Slide 10: AWS Resources Provisioned via Terraform​
VPC & Subnets: Custom VPC with 2 public and 2 private subnets
Networking:
Internet Gateway (for public access)
NAT Gateway with EIP (for private subnet access)
Route tables for public and private subnets
Security:
Web security group (for HTTP/SSH)
DB security group (restricted MySQL access from EC2)

## Slide 11: Compute & Database Automation
Title: EC2 and RDS Provisioning​
Content:​
EC2 Instance:​
Deployed in public subnet​
Apache installed using user_data​
RDS Instance:​
MySQL engine (version 5.7)​
Launched in private subnet group​
Attached security group for controlled access

## Slide 12: Task 4 – Security Considerations Report​
Challenge 1: Database Protection​
Problem: RDS databases that are accessible over the internet can be attacked using brute-force and SQL injection techniques.​ ​
​
Challenge 2: Controlled Web Access​
Problem: Application must be HTTP/HTTPS accessible but protected against unauthorized access.​ ​
Mitigation: ALB as public endpoint; web-sg allows HTTP (80) and HTTPS (443) only; SSH restricted to specific IP range.​ ​
Trade-offs: ALB and ASG raise costs; IP restrictions enhance security but limit access flexibility.​
Trade-offs: Increased complexity and cost from using a NAT Gateway. & Minor performance latency during patching.​

## Slide 13
Challenge 3: Secure Auto Scaling ​
Problem: When traffic increases, new instances need to have secure and consistent configuration applied.​
​Mitigation: ASG uses LT with AMI, SG, and cached user data so that new instances are automatically registered in the target ALB group.​
Trade-offs: Auto Scaling adds light latencies in both health checks and instance launch while using manual scaling which is faster but riskier and less secured.​
Additional Best Practices ​
IAM Roles: EC2 uses IAM roles for secure service access.​
Monitoring: CloudTrail and CloudWatch enabled for auditing and metrics.​
Encryption: RDS and ALB encrypted at rest and in transit.​
Backups: RDS set with 7-day backup retention for recovery.​
​
Conclusion ​
The infrastructure enhances security with private RDS subnets, public-facing ALB with secure SGs, and Auto Scaling with Launch Templates for consistent setup, balancing security, scalability, cost, performance, and operational complexity in AWS.​

## Slide 14
THANK YOU!!!